This Sunny solar electric car is driven by solar and electricity. The high-quality flexible solar module is equipped on the top, which is made by special process and dual-surface hyperbolic form with high photovoltaic conversion efficiency. It could be charging when it in sunshine and the endurance will increase 25%, and make battery cycling better, extend the life of the battery and reduce operating cost. This makes solar electric auto energy saving and environmental protection.

Sunny Golf Series Performance Parameter

| Model | Sunny PV-102 | Sunny /PV-204B | Sunny /PV-204 | Sunny /PV-204B | Sunny /PV-306 | Sunny /PV-408B |
| --- | --- | --- | --- | --- | --- | --- |
| Capacity | 2 person | 4 person | 4 person | 4 person | 6 person | 8 person |
| Max Speed (km/h) | 25 | 25 | 25 | 25 | 25 | 25 |
| Max Gradient | 25% | 25% | 25% | 25% | 25% | 25% |
| Continuous range(km) | 60-80 |
| Brake distance(m) | ≤2.5 | ≤2.5 | ≤3 | ≤3 | ≤3 | ≤3.5 |
| Min.Turing radius(m) | 3.3 | 3.3 | 3.5 | 3.5 | 3.5 | 3.5 |
| Exterior Size (mm) | 2370*1160*1760 | 2530*1160*1800 | 3400*1160*1900 | 3400*1160*1900 | 3900*1160*1950 | 3970*1160*1950 |
| Total Weight (Kg) | 400 | 470 | 500 | 500 | 570 | 600 |
| Steering | Geared, clearance auto-compensation |
| Battery (V) | 36,200Ah | 36,200Ah | 36,200Ah | 48,200Ah | 48,200Ah | 48,200Ah |
| Motor Power (Kw) | 2.2 | 2.2 | 3 | 3 | 3 | 3 |
| Controllor | Curtis |
| Charger(V) | 36V/48V,Computer intelligentize |
| Solar panel (W) | 170 | 170 | 170 | 170 | 150 | 150 |
| Frame | High strength steel tube welding structure |
| Material | Fiber plastic |
| Rear axle | CVT |
| Brake | Drum, mechanical |
| Tyre | 18x8.50-8 or 205/10-4PR |
| Ground clearance(mm) | 140 |
| Tread(mm) | 950 |
| 40’HC loading(Units) | 24 | 24 | 18 | 18 | 18 | 16 |
| FOBQingdao@USD | 4583 5350(solar) | 4733 5450 (solar) | 5343 6170(solar) | 5661 6388(solar) | 6423 7150 (solar) | 6573 7300 (solar) |

- PAYMENT:30% of the total amount as deposit should T/T to seller’s account after signing

this contact before production, balance should be clear before load the container. L/C is acceptable

- PACKING: Suitable for export.

- PORT OF LOADING: Qingdao, China

- DELIVERY TIME: About 20 working days after getting deposit.

- WARRANTY: One year for main parts

- PRICE VALIDITY: One month.

Note: ①Improvement is available according to your requirement.

②The first line are prices for electric cars; the second line are prices for solar electric cars.